## Slide 1
サクソン効果
ALLPPT.com _ Free PowerPoint Templates 、 Diagrams and Charts

## Slide 2
Parameters

## Slide 3: Physical properties
Gas phase | 
Viscosity | [Pa・s]
Density | 1 [kg/m3]
Solid phase | 
Density | 1250 [kg/m3]
Hamaker constant | 0.0
Spring constant | 50 [N/m]
Coefficient of restitution | 0.9
Coefficient of friciton | 0.3
Gas phase | 
Viscosity | 
Density | 1 [kg/m3]
Solid phase | 
Density | 1250 [kg/m3]
Hamaker constant | 0.0
Spring constant | 50 [N/m]
Coefficient of restitution | 0.9
Coefficient of friciton | 0.3

## Slide 4: Calculation conditions
Original particle size | 250 [μm]
Calculated particle size | 250 [μm]
Coarse grain ratio | 1
Number of particles | 500 、000
System | Mono-dispersed
Grid size | 0.5 [mm]
Calculation time | 0.2 [s]
Courant Number | 0.2
Iteration limit | 1
Inverse of sound velocity | 0.1 [mm/s]

## Slide 5: Object size
20
40
40
20
10
50
10
[mm]

## Slide 6
Comparison, Suction velocity

## Slide 7: Compared parameter
 | case1 | case2 | case3
Suction velocity | 100[mm/s] | 200 [mm/s] | 300 [mm/s]

## Slide 8: Comparison, Suction velocity
case1
100 [mm/s]
case2
200 [mm/s]
case3
300 [mm/s]
Color

## Slide 9: Comparison, Suction velocity
Epsilon
case1
100 [mm/s]
case2
200 [mm/s]
case3
300 [mm/s]

## Slide 10: Comparison, Suction velocity
結果
・ case1では、最下層(赤)が一段上の層(青)と混ざっている
・ case2とcase3では、それなりに層を保ったまま(混ざりあわず)落下している
・ case2と比べてcase3は発生する気泡領域が大きい
-> それに伴い、上部の層形状は変化している

## Slide 11: Comparison, Suction velocity
Suction velocity [mm/s] |  | 
100 | 200 | 300
sum | 142124 | 144739 | 145045
Number of partilces
in the area
層 | 5 |  | 37447 | 33510 | 31892
 | 4 |  | 33207 | 33215 | 32134
 | 3 |  | 28765 | 30313 | 30653
 | 2 |  | 22576 | 25159 | 26392
 | 1 |  | 20129 | 22542 | 23974

## Slide 12: Comparison, Suction velocity
結果・考察
・ 200,300[mm/s]を比較すると、そこまで粒子数に差がない
・ 速度が大きくなるほど、穴に入る粒子数が増加している
-> ある程度の速度で頭打ちになる
-> 圧力差による吸引力が強い

## Slide 13: Comparison, Suction velocity
Suction velocity [mm/s] |  | 
100 | 200 | 300
sum | 142124 | 144739 | 145045
層 | 5 |  | 26.34812 | 23.15202 | 21.98766
 | 4 |  | 23.36481 | 22.9482 | 22.1545
 | 3 |  | 20.23937 | 20.94322 | 21.13344
 | 2 |  | 15.88472 | 17.38232 | 18.19573
 | 1 |  | 14.16298 | 15.57424 | 16.52866
Number of particles rate
in the area [%]

## Slide 14: Comparison, Suction velocity
Number of particles rate
in the area [%]
Suction velocity [mm/s] |  | 
100 | 200 | 300
層 | 1 |  | 14.16298 | 15.57424 | 16.52866
 | 2 |  | 15.88472 | 17.38232 | 18.19573
 | 3 |  | 20.23937 | 20.94322 | 21.13344
 | 4 |  | 23.36481 | 22.9482 | 22.1545
 | 5 |  | 26.34812 | 23.15202 | 21.98766

## Slide 15: Comparison, Suction velocity
結果・考察
・ 100->200->300[mm/s] で、同じ間隔ではないが割合が変化していっている
・ 速度が大きくなるほど、下層粒子の割合が増加している
-> もう少し速度をあげれば、より綺麗に層ができる？
-> 圧力差による吸引力の影響と思われる

## Slide 16
Stationary Pestle

## Slide 17: Comparison, Suction velocity
Stationary
300 [mm/s]
Color

## Slide 18: Comparison, Suction velocity
Stationary
300 [mm/s]
Epsilon

## Slide 19: Comparison, Suction velocity
Number of partilces
in the area
Petle Type | 
Stationary | Move (300[mm/s]
層 | 5 |  | 36234 | 31892
 | 4 |  | 32809 | 32134
 | 3 |  | 30205 | 30653
 | 2 |  | 24198 | 26392
 | 1 |  | 21158 | 23974

## Slide 20: Comparison, Suction velocity
Petle Type | 
Stationary | Move (300[mm/s]
層 | 5 |  | 25.05739814 | 21.987659
 | 4 |  | 22.68886061 | 22.15450377
 | 3 |  | 20.88808055 | 21.13344135
 | 2 |  | 16.73397693 | 18.19573236
 | 1 |  | 14.63168377 | 16.52866352
Number of particles rate
in the area [%]